## Slide 1: Vehicle Tracking using IOV
Presented By:
Group 2:
Anik Das
510819023
Amit Kumar Shaw
510819012
Soham Pal
510819035
Guided By:
Prof(Dr.) Tuhina Samanta
Associate Professor
Department of Information Technology
IIESTS

## Slide 2: Introduction
Vehicle tracking using Internet of Vehicle – network of vehicles and roadside units
On the fly network formed, called ad-hoc network
This ad-hoc network of vehicles is called VANET

## Slide 3: What is vanet?
Wireless multi-hop network
Has a constraint of fast topology changes due to the high node mobility.
Enables a wide range of applications, such as congestion detection, prevention of collisions, safety, blind crossing, dynamic route scheduling, real-time traffic condition monitoring, etc.

## Slide 4: The Problem
Need of a system which tracks traffic and detects congestion in road
Current centralized solution has many drawbacks
Build an efficient system for this task

## Slide 5: Solution
Distributed system
V2V communication
Traffic congestion detection

## Slide 6: Implementation
Congestion Detection Algorithm with Adaptive Broadcasting

## Slide 7: Steps
Speed Monitoring
Congestion Detection
Localization
Aggregation
Broadcasting

## Slide 8: Speed Monitoring
Use speed as an indicator of congestion
Concept of threshold speed

## Slide 9: Congestion Detection
Calculation of Congestion Parameter, Cp = η * π
π = 0 if Vc > Vt or 1 if Vc < Vt
η = {1, 2, 3, 4, 5} depending on time interval
Congestion parameter value from vehicle's database is Cd

## Slide 10: Localization
Each street section has unique identification parameter Aid
This process retrieves the identification of the node’s current location and sets Aid parameter to this value
Included in BSM message with Cp and is used to store received data in vehicle's database

## Slide 11: Aggregation
Responsible for the adaptation of broadcast intervals
In case Vc < Vt : broadcast only if Cp > Cd
In case Vc > Vt : broadcast only if Cp ≠ Cd

## Slide 12: Broadcasting
Broadcast the message containing Cp and Aid parameters
All nodes who receive this message will know about traffic situation in Aid area
Following the previous steps, they can broadcast when necessary instead of doing it periodically

## Slide 13: Overall Algorithm At a glance

## Slide 14: Simulation Setup

## Slide 15: Recording of a congested street

## Slide 16: Metrics

## Slide 17: Drawbacks of current Implementation
Directional flow of traffic not considered
Possibility to optimize the number of emitted beacons

## Slide 18: Future Scope
Taking the directionality of traffic into account
01
Checking if the use of RSUs can reduce the load on the network traffic, shifting towards a hybrid (centralized + distributed) architecture
02

## Slide 19: conclusion
Investigated the effectiveness of VANET in capturing vehicle congestion.
Results showed the ability of the system to relay congestion data to all vehicles.
Simulation revealed that the VANET system was able to adapt to changing traffic conditions and maintain high performance.

## Slide 20: Thank you